## Slide 1: Frequency-dependent attenuation in fractional Helmholtz wave equations
State of progress
Samuel Rouah-Sayag

## Slide 2: Ultrasound: general characteristics
Sound wave above hearing range (20 kHz).
Range: 20 kHz to more.
A wide range of application
  Testing materials
  Range finding (measuring distance)
  Identification of objects
  Imaging
  Microscopy
  Processing of materials
Picture Authoring: "Ultrasound range diagram" by Ultrasound_range_diagram.png: Original uploader was LightYear at en.wikipediaUltrasound_range_diagram_png_(sk).svg: Original uploader was LightYear at en.wikipediaderivative work: Coolth (talk) - Ultrasound_range_diagram.pngUltrasound_range_diagram_png_(sk).svg. Licensed under CC BY-SA 3.0 via Wikimedia Commons - https://commons.wikimedia.org/wiki/File:Ultrasound_range_diagram.svg#/media/File:Ultrasound_range_diagram.svg

## Slide 3: Medical ultrasound
Purpose of imaging.
Different modes (A, B, C, M, Doppler…).
Transducer active/passive
Steps to form an image:
  Emission of a piezoelectric transducer.
  Reception of the same transducer (time, intensity)
  Time ≈ travel time (how deep)
  Intensity ≈ brightness (how dense)
B-Mode (Brightness mode)
2D (B-Mode) and 3D picture of an embryo obtain with ultrasound (Michpala Meuhedet, Jerusalem, 2013).

## Slide 4: Trade-off
Advantage
  Ultrasound is cheap
  (Medical) ultrasound is non destructive
  It makes of it a tool of choice for sensitive diagnostics
Problem
  Lack of precision due to the physics of measured phenomena and the targeted tissues.
  Compromise in the calculation to obtain a human readable information (hard coded constant).
  Type of machine and transducers (its geometry).
Possible solution TOMOGRAPHY
More complex. Require a better understanding and modelling of the underlying physics

## Slide 5: The physics of the problem

## Slide 6: Speed of sound and power law attenuation
Resolution is obtained at high frequency
Depth is obtain a low frequency
Resolution and depth constitute a trade off
Attenuation is a constant not available in B-Mode
Figure 1: Detection and characterization of breast masses as a function of attenuation and speed of sound

## Slide 7: Speed of sound and power law attenuation
Attenuation function of:
  a vector position (1D, 2D, 3D)
  is the angular frequency (
  and are non negative location dependent parameters.
If the material is homogeneous
typically ranges between 1-2

## Slide 8: Fractional wave equation
Equation describes a wave of pressure.
pressure function of location and time.
is the speed of sound.
the location dependent attenuation.
the material and location dependent parameter.
= 0: (wave equation)

## Slide 9: Fractional wave equation: the treatment
Fractional derivative equation are studied but the theory is rather complicated.
We switch the space-time basis with space-frequency with Fourier transform
is now the location and frequency dependent pressure wave.
  is the angular frequency (
We benefit from the operation in the Fourier basis

## Slide 10: Helmholtz equation
The time derivative terms powers are now products factors.
We obtain the Helmholtz equation
If
We define a refractive index:
Let us formulate the equation in a simpler form
Speed and material are completely integrated in the index.

## Slide 11: Helmholtz equation: the treatment
Postulate a solution of the form:
is the amplitude, is the travel time
Develop and obtain equations:
First possibility: highly oscillating system
Second possibility: low to averagely oscillating system

## Slide 12: Highly oscillating system
Approximation may be neglected in high frequency ( is high)
The system (the pair of two way coupled equation) become:
The strategy is to:
  Solve the Eikonal equation and obtain (matrix).
  Solve the second equation with and obtain
  Check if the approximation is consistent.

## Slide 13: Low to averagely oscillating system
If is relatively low (the frontier has to be determined), the preceding approximation cannot be made
Subsequently the complexity of the system of the two equations:
…is equivalent to the complexity of the Helmholtz equation
Strategy:
  Solve directly the Helmholtz equation on a closed case to validate a method.
  Introduce the refractive index as , ].
  Check consistency of the model.

## Slide 14: Project goal: tackle low and intermediate frequency
Explore and compare several methods to solve the forward problem.
High frequency hypothesis: ray approximation to the wave front propagation. Solve the Transport Equation coupled to the Eikonal equation - one-way-coupling.
The ultimate method and goal of the project is the solution of the full-wave Helmholtz equation.
Build a tool.
Conduct numerical simulations to evaluate the results.

## Slide 15: BVP: Boundary Value Problem
BVC (Boundary Value Condition) of
Dirichlet
Neumann BVC
Cauchy BVC
Robin BVC

## Slide 16: BVP: Boundary Value Problem
Source is Dirichlet
Sommerfeld
Damping technique

## Slide 17: Available methods and the chosen method

## Slide 18: Finite Differences Method (FDM)
The operator (the equation) and its parameters are known.
We define a region (possibly time range) on it we want to solve the equation.
We seek an approximation of the operator by “replacing the derivatives in the differential equation by finite difference approximation” (Leveques, 2007).
  There is approximation as also error.
  The replacing formulas is found according to the desired order of precision thanks to Taylor theorem.
Different methods exist that fit to the type of operator that is dealt with: parabolic, hyperbolic, elliptic.

## Slide 19: Finite elements method (FEM)
The operator, its parameters and BVC are known.
A region and its frontier over it we want to solve the equation.
A functional (generally an integral) is derived from both the equation and its boundary condition.
The region is divide in simple shape (triangle, rectangle…).
To each division is adjoined a simple polynomial
The purpose is to minimize over .
Advantage:
  Very variable boundary condition may be applied.
  The geometry may involve irregularly shaped boundaries.
  Modification of the equation are easily handled

## Slide 20: Spectral Method (SM)
Very closed in its approach to the FEM
The operator, its parameters and BVC are known.
A region and its frontier over it we want to solve the equation.
The solution is written as a sum of basis function (typically in the basis of Fourier, Lagrange…) with unknown coefficient.
This solution is set in the equation and lead to another function that may be treated numerically (there is no unique method).
In spectral method the solution is one function over the whole domain express in different basis while in FEM the solution is a sum of function.

## Slide 21: Study of the FDM (Finite Difference Method)
Reference:
LeVeque R J., Finite Difference Methods for Ordinary and Partial Differential Equations. Philadelphia: Society for Industrial and Applied Mathematics (SIAM), 2007.
Burden R L. and Faire J D, Numerical Analysis, 9th ed.: Brooks/Cole, 2010.
S C Chapra and R P Canale, Numerical Methods For Engineers, Sixth Edition ed., Mac Graw Hill, Ed., 2010

## Slide 22: From the derivation
Illustration: Finite Difference Methods for Ordinary and Partial Differential Equations, Leveque, 2007.

## Slide 23: From Taylor
Taylor Theorem (1712 !)
(1)
(2)
(3)
Derived | Scheme | Type | Order
(1) |  | Forward | 
(2) |  | Backward | 
(1)+(2) |  | Central | 
2(1)-6(2)+(3) |  | Notname | 
(1)+(2) |  | Symmetric | 
Derived | Scheme | Type | Order
(1) |  | Forward | 
(2) |  | Backward | 
(1)+(2) |  | Central | 
2(1)-6(2)+(3) |  | Notname | 
(1)+(2) |  | Symmetric | 

## Slide 24: Error
Example: , and we want an approximation a of the first derivative ().
'h' 'Back Err' 'Forw Err'
[1.0000e-01] [-4.1138e-02] [4.2939e-02]
[5.0000e-02] [-2.0807e-02] [2.1257e-02]
[1.0000e-02] [-4.1983e-03] [4.2163e-03]
[5.0000e-03] [-2.1014e-03] [2.1059e-03]
[1.0000e-03] [-4.2065e-04] [4.2083e-04]
'Cent Err' 'du_3_err'
[9.0005e-04] [-6.8207e-05]
[2.2510e-04] [-8.6491e-06]
[9.0050e-06] [-6.9941e-08]
[2.2513e-06] [-8.7540e-09]
[9.0050e-08] [-6.9979e-11]

## Slide 25: Errors: truncation
Big-O
This may be a representation we can use to compare scheme between each others.
Leveque (2007) also demonstrate error of the scheme is the same that the cumulative error.

## Slide 26: PDE Poisson
Elliptic PDE (stationary) so is Helmholtz
with
Study of the book:
Numerical methods for engineers, 6th ed., S.C Chapra, R.P Canale
Numerical Analysis, 9th ed., R.L Burden, J.D Faires

## Slide 27: Results
Use of the five point stencil with
the preceding described scheme
L = i + (m-j) * n;
L1: 4 -1 0 -1 0 0 0 0 0 25
L2: -1 4 -1 0 -1 0 0 0 0 50
L3: 0 -1 4 0 0 -1 0 0 0 150
L4: -1 0 0 4 -1 0 -1 0 0 0
L5: 0 -1 0 -1 4 -1 0 -1 0 = 0
L6: 0 0 -1 0 -1 4 0 0 -1 50
L7: 0 0 0 -1 0 0 4 -1 0 0
L8: 0 0 0 0 -1 0 -1 4 -1 0
L9: 0 0 0 0 0 -1 0 -1 4 25
sol=
18.75 37.50 56.25
12.50 25.00 37.50
6.25 12.50 18.75

## Slide 28: Poisson (suite)
If the result is more precise…

## Slide 29: Exact finite difference scheme for the Helmholtz equation
Study of the article:
Wong Yau Shu and Li Guangrui, Exact Finite Difference Schemes for Solving Helmholtz Equation at Any Wavenumber, Institute for Scientific Computing and Information, Ed.: International Journal of Numerical Analysis and Modeling, 2001, vol. 2.
Hegedus G. and Kuczmann M., Calculation of the Solution of Two-Dimensional Helmholtz Equation.: Acta Technica Jaurinensis, 2010, vol. 1.

## Slide 30: 1D problem
Standard scheme (Taylor)
Central point:
Sommerfeld (right):
Sommerfeld (left):
New scheme(Taylor and series)
The scheme is exact i.e. it does not have any truncation error.

## Slide 31: Program
Building of a first generic program to handle this problem parameterised by:
  The type of scheme
  Sommerfeld Boundary Condition (left or right)
  Dirichlet Boundary Condition
  the coordinate of the grid for example
The error is the infinite norm:
Analytical solution:
The program integrate a standard scheme for the comparison. The central point is classical and the Sommerfeld scheme has been search.

## Slide 32: Results
It is possible to reproduce results of the article.
h = 0.01
error1 =
'k' 'SFD' 'NFD' 'SFD' 'NFD'
[ 10] [0.0048] [0.0017] [0.0040] [4.5521e-14]
[ 30] [0.1106] [0.0150] [0.1137] [1.2969e-14]
[ 50] [0.5371] [0.0431] [0.5267] [8.2523e-15]
[ 70] [1.3487] [0.0841] [1.3859] [1.5922e-14]
[100] [1.9998] [0.1814] [1.9998] [1.0716e-14]
[150] [2.4932] [0.3963] [2.1038] [1.4453e-14]

## Slide 33: 2D problem
Standard scheme (Taylor)
Central point:
Side point (4 schemes):
Corner point (4 schemes):
New scheme(Taylor and series)
The scheme use a Bessel function of the first kind:
There is one scheme for the central point, 4 scheme for the side and 4 scheme for the corners to integrate Sommerfeld.

## Slide 34: Program
Building of a second generic program to handle this problem parameterised by:
  The type of scheme (new, standard)
  The Bessel function and its derivations (integral, exact theta)
  Boundary condition (left and/or right) Dirichlet or Sommerfeld
  the coordinate of the grid for example
The error is the infinite norm:
Analytical solution:
The program integrate a standard scheme for the comparison. The central point is classical and the Sommerfeld scheme has been search this time with the help of the publication of another team.

## Slide 35: Results
Analytical fonction:
h: 0.0200
res_tab =
'' '' 'E inf' 'E inf' 'J0(kh)' 'J0(kh)'
'kh' 'k' 'SFD' 'NFD' '[0,pi]' 'Exact Theta'
[0.8485] [42.4264] [25.0648] [12.1595] [0.8279] [ 0.8253]
[0.7071] [35.3553] [14.3569] [ 7.0017] [0.8789] [ 0.8776]
[0.5657] [28.2843] [ 7.2401] [ 3.5638] [0.9216] [ 0.9211]
[0.4243] [21.2132] [ 3.0220] [ 1.4996] [0.9555] [ 0.9553]
[0.2828] [14.1421] [ 0.8713] [ 0.4450] [0.9801] [ 0.9801]
[0.1414] [ 7.0711] [ 0.1053] [ 0.0543] [0.9950] [ 0.9950]

## Slide 36: Result: Bessel
Three possible version (from the article):
'kh' 'k' 'sum [0,pi]''exact theta''matlab'
[0.8485][42.4264][ 0.8279][ 0.8253][0.8279]
[0.7071][35.3553][ 0.8789][ 0.8776][0.8789]
[0.5657][28.2843][ 0.9216][ 0.9211][0.9216]
[0.4243][21.2132][ 0.9555][ 0.9553][0.9555]
[0.2828][14.1421][ 0.9801][ 0.9801][0.9801]
[0.1414][ 7.0711][ 0.9950][ 0.9950][0.9950]
'J0(kh)' 'J0(kh)' 'J0(kh)'
'sum [0,pi]''exact theta''matlab'
[ 3.3118][ 3.3013][3.3118]
[ 3.5154][ 3.5103][3.5154]
[ 3.6863][ 3.6842][3.6863]
[ 3.8220][ 3.8213][3.8220]
[ 3.9204][ 3.9203][3.9204]
[ 3.9800][ 3.9800][3.9800]

## Slide 37: Results
Analytical function:
Different Bessel functions:
'kh' 'SFD' 'NFD-J0[0,pi]''NFD-J0[pi/8,3pi/8]''NFD - exact theta'
[42.4264] [25.0648][ 12.1595][ 4.4379][ 3.4574e-13]
[35.3553] [14.3569][ 7.0017][ 2.5483][ 4.1767e-13]
[28.2843] [ 7.2401][ 3.5638][ 1.2956][ 3.3647e-13]
[21.2132] [ 3.0220][ 1.4996][ 0.5450][ 3.8106e-13]
[14.1421] [ 0.8713][ 0.4450][ 0.1617][ 1.5676e-13]
[ 7.0711] [ 0.1053][ 0.0543][ 0.0197][ 1.4720e-12]
Full Dirichlet (all side, same problem)
'kh' 'SFD' 'NFD-J0[0,pi/2]''NFD-J0[pi/8,3pi/8]''NFD - exact theta'
[42.4264] [72.8404][ 19.0699][ 9.8070][ 1.0542e-12]
[35.3553] [22.1503][ 11.3565][ 3.1691][ 3.4689e-13]
[28.2843] [39.6772][ 9.8812][ 3.1514][ 6.9322e-13]
[21.2132] [40.1207][ 7.1648][ 3.0067][ 1.5089e-12]
[14.1421] [ 1.0660][ 0.5276][ 0.1920][ 1.1014e-13]
[ 7.0711] [ 0.2368][ 0.1198][ 0.0434][ 3.2334e-12]

## Slide 38: Results
Analytical function:
Fix but

## Slide 39: Search for theta
Least-square algorithm
  Determine the coefficient of the linear system by calculating is it and ? N.R).
  Solve the system by GMRES (or another solver)
  Take partial data from (we take the two lines besides the Dirichlet boundaries in this study) and form the least square function: where are the data from and are the exact solution of plane wave with parameter .
  Estimate using a non-linear least square (algorithm N.R) such as the Levenberg-Marquardt algorithm. Using different approximation in Step 4, we determine and .
  Update the coefficient of the system by re-computing
  Repeat 2-5 until converge.
The implementation has been done with Dirichlet given the problems in the formulation and the impossibility to find a good explanation for the Sommerfeld boundary.
It match within to iteration (that is in contradiction with the article). Other angles are much more problematic.

## Slide 40: High order finite difference schemes
References: